## Slide 1
microcontroller
beginner workshop
PICO
Instructor: Amytis Saghafi

## Slide 2
What is a Microcontroller?
Microcontroller vs. Single Board Computers
The variety of boards
MicroPython vs C
Software Setup
Agenda
Electronic Basics
Hands-on Tutorials
blinking an LED
Using a Button
possibly: PWM and ADC

## Slide 3
a small computer on a single integrated circuit, designed for embedded applications.
What is a Microcontroller?

## Slide 4
RAM
Central Processing Unit
Components of a Microcontroller
ROM
I/O Peripherals
ADC
DAC
Serial Port

## Slide 5
Microcontroller vs. Single Board Computer
Microprocessors
(MPUs)
Microcontrollers
(MCUs)
Single Board Computers
(SBC)

## Slide 6
Variety of Boards
Arduino
Raspberry Pi Pico
STM 32

## Slide 7
MicroPython
Ease of use: Easy
Setup: Drag-drop UF2
Performance: Good enough
Hardware access: High-level Abstraction
Debugging: REPL / print
C/ C++ (Pico SDK)
Ease of Use: Moderate (requires compilation)
Setup Time: Slower (CMake and toolchain setup)
Performance: Max performance (up to ~250× faster)
Control: Direct register and hardware access
Debugging: SWD, debug probes, and GDB
VS

## Slide 8
Raspberry Pi Pico
Powerful Hardware
Dual-core ARM Cortex-M0+
Up to 133 MHz
264 KB RAM
Lots of Feature
26 GPIO pins
ADC, PWM, I²C, SPI, UART
Programmable I/O (PIO)
Why Raspberry Pi Pico?
Easy development
Supports MicroPython and C/C++
Simple setup with Thonny

## Slide 9
Install Thonny IDE from: https://thonny.org/
Open Thonny, go to tools→ options → Interpreter
Change “Local Python 3” to “MicroPython (Raspberry Pi Pico)”
Select Micropython (Raspberry Pi Pico)
Hold the BOOTSEL button
Plug the Pico into USB.
Flash Pico (Instructions coming in the next few slides)
Software Setup
BOOTSEL

## Slide 10
Once Pico is plugged into USB it should show up as a flashdrive!

## Slide 11
Then Open Thonny and Click on the backend in the bottom right corner, then select “Install MicroPython”

## Slide 12
Choose the name that showed up as a drive as target Volume
and Pico W/WH as the variant and install
Wait for the pico to reboot! (no need to unplug)
Once rebooted you should be able to select it as a backend with a communication port attached to it.
Note: If this process doesn’t work, you can download the file directly from the Raspberry Pi Pico website and drag it on to the flashdrive. This will automatically reboot the pico and should work as normal.

## Slide 13
Blink onboard LED
Onboard LED
Pin Access
Timing Functions

## Slide 14
GPIO = General Purpose Input/ Output
What is GPIO?
Uses digital input (1 and 0)
As input, peripheral requires external power
As output, typically provides peripheral with some sort of power
note: sometimes external power is still required

## Slide 15
Electronics Basics
OHM’S LAW: V=IR
Pico GPIO pin voltage: 3.3 V
LED voltage drop: 2.0 V
Safe LED Current: 10-30 mA
R=
3.3 V - 2.0 V
0.02 A
= 65 Ω
Choose closest value available!
(I used 220 Ω)

## Slide 16
Hands-On Tutorials
Wire up an LED to a GPIO pin
Write MicroPython Program to Blink the LED
Play with Blink timing
Blink LED
What are pull-up and pull-down resistors? (look it up and we will discuss later!)
Wire up a Button to a GPIO pin
See if you can output a message when button status changes!
Write a program that uses the button to control the LED
You can add more buttons and LEDs and play around with the functionality!
Set-up button
3V3(OUT)
Pull-UP
Resistor
(10 kΩ)
GPIO Pin
3V3(OUT)
Pull-Down
Resistor
(10 kΩ)
GPIO Pin
GPIO Pin
R
(220 Ω)
LED
(Default: 0)
(Default: 1)

## Slide 17
CHALLENGE: Reaction Timer Game
Write program that:
Waits random delay
Turns on LED
Records how fast button was pushed after LED turns on
Prints reaction time in console
Keeps track of best reaction time of the session

## Slide 18
PICO PINOUT

## Slide 19
PWM = Pulse Width Modulation
What is PWM?
This is how we control brightness!

## Slide 20
What is ADC and how is it used?
ADC = Analog to digital converter
reads voltage as an 16-bit number (0 -65536)
3V3(OUT)
ADC Pin
Photoresistor
R1
10 kΩ

## Slide 21
CHALLENGE: Automatic Light Control
Wire up a photoresistor to an ADC pin. (use a voltage divider)
Write a program that:
  Reads light levels from the photoresistor using the ADC pin
  Adjusts the brightness of the LED using PWM based on light level readings
  (BONUS) play around with a manual button override!

## Slide 22
Thanks for coming!
Any Questions?
Please return your kits the way you found the :)